## Slide 1
Solar as a Business
PM-KUSUM Component C & the AI-Lab Alternative
Feeder-Level Solarisation (FLS) as a developer · 1 MW economics · break-even reality · a hybrid way in
Decision brief · September 2026 · Based on a Karnataka (HESCOM) sample study, an Indian energy think-tank consultation and installation SMEs
Figures are 1 MW thumb rules for decision-making, not a bankable model. All data points referenced on the slide or in notes.
Notes: Purpose: decide whether to enter PM-KUSUM Component C as a developer, and whether a hybrid FLS + AI-lab structure improves the case. Audience: two decision-makers. 13 slides.

## Slide 2
PM-KUSUM Component C in one page
Solarising the electricity that already runs farm pumps
THE PROBLEM
▪ Farm pumps run on grid power that the state sells at near-zero tariffs
▪ That subsidy is one of the largest recurring drains on state DISCOM budgets
▪ Supply is unreliable; diesel fills the gap
THE FIX (COMPONENT C)
▪ FLS – one solar plant feeds an entire 11 kV agricultural feeder serving many pumps
▪ IPS – a farmer solarises their own single pump
▪ Daytime pump load runs on sun; surplus is sold to the DISCOM
WHO PAYS WHOM
▪ Centre (MNRE): 30% CFA – Rs 1.05 cr per MW, paid after commissioning
▪ DISCOM: signs a 25-year PPA and buys every unit
▪ Farmer: leases land, earns rent, keeps farming
▪ Developer: funds, builds, owns, operates
35 lakh
grid-connected pumps targeted under Component C
Rs 1.05 cr / MW
central subsidy (30% of Rs 3.5 cr benchmark)
25 years
fixed-tariff power purchase agreement
0.5 – 2+ MW
typical FLS plant size, ~5 acres per MW
Why MNRE pushes Component C: it is the direct fix for the agricultural power subsidy, it touches the largest number of farmers, and it is the component that fell furthest behind – which is exactly why PM-KUSUM 2.0 is being redesigned around it.
Sources: MNRE PM-KUSUM guidelines; Down To Earth (Centre readies PM-KUSUM 2.0); PIB – FLS guidelines under Component C
GreenWealth · PM-KUSUM Component C · 2/15
Notes: https://mnre.gov.in/en/pradhan-mantri-kisan-urja-suraksha-evam-utthaan-mahabhiyaan-pm-kusum/
https://www.downtoearth.org.in/energy/centre-readies-pm-kusum-20-as-focus-shifts-to-feeder-level-solarisation
https://pib.gov.in/Pressreleaseshare.aspx?PRID=1678286

## Slide 3
Our entry: the developer route
We do not make panels. We assemble land, capital and a DISCOM contract.
1 LANDOWNERS
Identify farmers within ~5 km of an agri substation; sign 25-year lease (Rs 25–50k / acre / yr, 3% escalation)
2 ASSOCIATION
Form the SPV / LLP; JV with an empanelled EPC for track record; bank lines and guarantees
3 DISCOM
Register land against the substation; bid the FLS tender (L1 tariff wins)
4 BUILD & COMMISSION
~12 months; CFA released on COD against bank guarantee
5 EARN / EXIT
25-yr PPA cash flows – or sell the SPV to an InvIT once it is operating
WHY THE FARMER DOESN'T DO THIS HIMSELF
▪ Cannot raise Rs 3–4 cr per MW at a workable rate; would have to mortgage the land he lives on
▪ Tenders set net-worth, track-record and bank-guarantee gates that exclude individuals
▪ DISCOM wants one accountable counterparty for 25 years, not 40 smallholders
▪ He wants rent and to keep farming – not to run a power plant
WHAT WE BRING
▪ Institutional cost of capital and bank guarantees
▪ Land aggregation across many small parcels into one bankable site
▪ EPC / procurement / interconnection / compliance – via partner until in-house
▪ 25-year O&M capability and a portfolio that spreads risk
Sources: MNRE FLS guidelines (RESCO mode, model PPA & lease); Heaven Green Energy – KUSUM tenant-farmer rules; Component C RfS documents (MSEDCL, MPUVNL)
GreenWealth · PM-KUSUM Component C · 3/15
Notes: RfS documents allow consortium/JV of up to 2 members; LLPs are eligible bidders. Land registration portal: farmer selects nearby 33/11 kV substation, uploads title, pays ~Rs 1,000 + GST.

## Slide 4
What we have already done
Think-tank consultation · installation SMEs · a Karnataka (HESCOM) sample study
CONSULTED
▪ An Indian energy-policy think tank on scheme design, tariff trajectory and 2.0 direction
▪ Installation SMEs (EPC contractors) on real build cost, timelines and O&M
▪ Cross-checked against MNRE / KERC / TNERC orders and tender documents
KARNATAKA SAMPLE STUDY (HESCOM)
▪ 4,852 11 kV feeders in the July-2026 register
▪ 3,029 pure AGRICULTURE feeders across 6 districts
▪ 401 parent substations identified; 287 located to high confidence
▪ 2,244 agri feeders mapped to satellite imagery
▪ Mudhol (Bagalkot)*: 17 substations, 199 agri feeders – densest cluster; 5 biggest sites within ~10–14 km of each other
Shirol 110/11 kV substation, Mudhol taluk* – 18 agri feeders. Pin = KPTCL compound (Google Maps POI).
5.0–5.5
kWh/m²/day GHI, N. Karnataka
300–330
clear sunny days per year
1,600–1,850
kWh per kWp per year
WHAT THE FIELD WORK CHANGED IN OUR THINKING
Feeders are lines, not points – siting is about substations. Land within 5 km of a high-feeder-count substation is the scarce input, and ~55% of cultivators are tenants who cannot sign a lease. Coordinates are Google-derived: suitable for shortlisting; ground validation precedes any land commitment.
* Mudhol / Bagalkot is a TENTATIVE area – identified through our own open-source desk research only; not a validated or chosen site. Sources: HESCOM feeder register (Jul 2026); IISc CES; Qbits irradiance data; Google Maps Platform
GreenWealth · PM-KUSUM Component C · 4/15
Notes: https://wgbis.ces.iisc.ac.in/biodiversity/pubs/ces_tr/TR132/solarenergy.htm
https://qbitsenergy.com/blog/solar-irradiance-data-india-statewise/
Workbook: HESCOM_AGRI_11kV_Feeders_GEOCODE_READY.xlsx; Atlas: HESCOM_KUSUM-C_Feeder_Site_Atlas_GreenWealth.pptx

## Slide 5
Data slide 1 – the economics of 1 MW
Thumb rules we are using, and where each number comes from
ITEM
1 MW
BASIS / SOURCE
Capital cost, all-in (panels, structure, inverters, evacuation, land dev, IDC, contingency)
Rs 4.5 cr
Thumb rule from installation SMEs; MNRE benchmark is Rs 3.5 cr/MW
Central subsidy (CFA) – 30% of benchmark, paid AFTER commissioning
Rs 1.05 cr
MNRE: Rs 1.05 cr/MW; capped at benchmark or tender cost, whichever lower
Our net capital at risk
Rs 3.45 cr
Rs 4.5 cr – 1.05 cr (full Rs 4.5 cr must be funded up-front)
Generation, conservative
1.5 million units / yr
≈17% CUF; N. Karnataka can reach 1.6–1.85 million
Tariff assumed
Rs 3.00 / unit
KERC generic Rs 3.07; HESCOM Component-C ceiling was Rs 2.13
Revenue
Rs 45 lakh / yr
1.5 M units × Rs 3
Operating cost (O&M, 5-acre lease, insurance, admin)
Rs 8.5 lakh / yr
Escalates ~3%/yr; steps up after year 5
Net cash per year
Rs 36.5 lakh
≈ 10.6% cash yield on net capital, before debt service and tax
Simple payback on net capital: Rs 3.45 cr ÷ Rs 36.5 lakh ≈ 9.5 years – about 12 once maintenance steps up and inverters are refreshed. Even at MNRE's Rs 3.5 cr benchmark it is ~7 years. A 3-year payback would need ≈ Rs 5.3 / unit – a tariff India has not paid for solar since ~2015.
Sources: MNRE benchmark & CFA (Down To Earth, Jan 2026); KERC generic tariff order 2025-26 (Mercom); HESCOM 108 MW Component-C RfS ceiling Rs 2.13 (SolarQuarter, Dec 2025); SME inputs
GreenWealth · PM-KUSUM Component C · 5/15
Notes: https://www.mercomindia.com/karnataka-sets-benchmark-tariff-of-%E2%82%B93-07-kwh-for-mw-scale-solar-projects
https://solarquarter.com/2025/12/11/hescom-invites-bids-for-108-mw-solar-projects-under-pm-kusum-in-karnataka/
https://www.downtoearth.org.in/energy/centre-readies-pm-kusum-20-as-focus-shifts-to-feeder-level-solarisation
Opex build-up: O&M Rs 4.5 L, lease 5 acres x Rs 50k = Rs 2.5 L, insurance Rs 0.7 L, admin Rs 0.8 L.

## Slide 6
Returns from the DISCOM alone – 1 MW
Cumulative net cash, Rs crore. CFA lands in year 1; maintenance steps up from year 6; inverter refresh in year 10
Chart: Cumulative net cash (Rs crore)
| Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7 | Y8 | Y9 | Y10 | Y11 | Y12 | Y13 | Y14 | Y15
All-in capex Rs 4.5 cr → break-even ≈ year 11.8 | -4.5 | -3.085 | -2.725 | -2.369 | -2.019 | -1.674 | -1.373 | -1.078 | -0.79 | -0.508 | -0.484 | -0.216 | 0.046 | 0.3 | 0.547 | 0.786
MNRE benchmark capex Rs 3.5 cr → break-even ≈ year 7.3 | -3.5 | -2.085 | -1.725 | -1.369 | -1.019 | -0.674 | -0.373 | -0.078 | 0.21 | 0.492 | 0.516 | 0.784 | 1.046 | 1.3 | 1.547 | 1.786
WHAT THE CURVE SAYS
▪ Year-1 dip is Rs 4.5 cr out, Rs 1.05 cr back
▪ Then ~Rs 0.35 cr a year, slowly eroding (degradation, opex escalation)
▪ Break-even: 7 years at best, ~12 years on realistic capex
▪ Year-15 cumulative: Rs 0.8 cr (all-in) / Rs 1.8 cr (benchmark)
WHO THIS SUITS
▪ Infrastructure capital at 7–9% cost of funds: pension funds, InvITs
▪ Groups with an EPC arm (margin in year 1) and a tax base to use 40% accelerated depreciation
▪ Not a 3–5 year private-capital return on its own
Model: 1.5 M units/yr, Rs 3/unit, 0.5%/yr degradation, opex Rs 8.5 L escalating 3%, ×1.4 from year 6, Rs 25 L inverter refresh year 10, no debt, no tax. Illustrative, not bankable.
GreenWealth · PM-KUSUM Component C · 6/15
Notes: Cumulative series (Rs cr): all-in [-4.5, -3.085, -2.725, -2.369, -2.019, -1.674, -1.373, -1.078, -0.79, -0.508, -0.484, -0.216, 0.046, 0.3, 0.547, 0.786]; benchmark [-3.5, -2.085, -1.725, -1.369, -1.019, -0.674, -0.373, -0.078, 0.21, 0.492, 0.516, 0.784, 1.046, 1.3, 1.547, 1.786].

## Slide 7
Data slide 2 – what the market is telling us
Scheme progress, tariff benchmarks, and who buys finished plants
31%
of PM-KUSUM's 34.8 GW target achieved (≈10.95 GW, Dec 2025)
20%
Component A: 1,986 MW installed of 10,000 MW (Jul 2026)
Rs 2.13
per unit – HESCOM Component-C tender ceiling (Dec 2025)
Rs 3.07
per unit – KERC generic MW-scale solar tariff 2025-26
THE SCHEME IS BETWEEN VERSIONS
▪ PM-KUSUM 1 closed – minister's statement, 7 Aug 2026; projects with PPAs by 31 Dec 2025 have until 31 Mar 2027
▪ PM-KUSUM 2.0 not yet notified – ~Rs 50,000 cr outlay, 10 GW agrivoltaics, battery storage, 'better subsidies'
▪ Karnataka's own programme: 3 GW / Rs 10,500 cr feeder solarisation, 2,777 MW targeted this year
FINISHED PLANTS DO HAVE BUYERS
▪ IndiGrid (KKR): 300 MW solar for Rs 1,550 cr – Rs 5.17 cr/MW (Aug 2026)
▪ Brookfield Bikaner 550 MW: ~Rs 3,000 cr bids from Actis, IndiGrid, INOXGFL – Rs 5.45 cr/MW
▪ Only 2.7% of India's operating utility solar is in InvITs – buyer base far from saturated
READ-ACROSS FOR US
▪ Under-achievement is the industry voting with its wallet: at Rs 2.13/unit with DISCOM payment delays, capital stayed away. Our 7–12 year break-even is not pessimism – it is what the market concluded.
▪ Exit values track tariff: ~Rs 5.2 cr/MW deals are consistent with ~Rs 3/unit assets. A Rs 2.13 asset is worth materially less to an InvIT.
▪ Timing: with 1.0 closed and 2.0 pending, the coming 6–9 months are a preparatory window – land, EPC capability and entity structure progress independent of 2.0's terms.
Sources: Saur Energy (MNRE data, Mar 2026); newsonair / MNRE (Jul 2026); SolarQuarter; Mercom; ANI (7 Aug 2026); Renewable Watch (Mar 2026); Business Standard; Whalesbook; bne IntelliNews
GreenWealth · PM-KUSUM Component C · 7/15
Notes: https://www.aninews.in/news/business/pm-kusum-2-likely-to-be-rolled-out-soon-says-union-minister-pralhad-joshi20260807122725/
https://renewablewatch.in/2026/03/10/karnataka-introduces-new-feeder-level-solarisation-programme-in-state-budget-2026-27/
https://www.business-standard.com/companies/news/indigrid-acquires-solar-power-plant-at-an-enterprise-value-of-rs-1-550-cr-124022301117_1.html
https://www.whalesbook.com/news/English/energy/Actis-IndiGrid-INOXGFL-Eye-Brookfields-indian-rupee3000-Cr-Green-Asset/6a57edd85cb7edf90c320e66
https://www.intellinews.com/india-s-green-energy-invits-boom-is-waiting-to-happen-460838/
https://www.deccanherald.com/india/pm-kusum-scheme-faces-implementation-hurdles-only-30-targets-met-as-deadline-nears-report-3141583

## Slide 8
The downside – and why starting late may be smarter
What a 25-year asset actually does to you in years 5 to 10
YEAR 5+ : THE MAINTENANCE CLIFF
▪ Inverters / rectifiers approach end of design life; failures rise; a full refresh (~Rs 25 L/MW) typically lands in years 8–12
▪ Any battery (if we add BESS) is a 6–10 year asset – replacement is a second capex
▪ Module degradation 0.5%/yr compounds; cleaning water in N. Karnataka is a real constraint
YEAR 5–7 : TECHNOLOGY REVISION
▪ Module efficiency keeps stepping up (19% → 23%+); Rs/W keeps falling
▪ Our tariff is frozen for 25 years – newer entrants bid cheaper and DISCOMs compare
▪ Storage and agrivoltaics in 2.0 may reset what a 'good' plant looks like – and what it is worth on exit
STRUCTURAL
▪ DISCOM receivables of 60–180 days are common – the biggest real-world risk
▪ Fixed nominal tariff vs 25 years of inflation
▪ Land title: ~55% of cultivators are tenants who cannot sign; disputes surface late
▪ Illiquid: exit takes months and depends on InvIT appetite
WHY A LATER START CARRIES LESS RISK
▪ 2.0 terms move the economics. A higher subsidy, or one paid at milestones instead of only after COD, shrinks the up-front funding gap on slide 5. A storage premium would retire the Rs 2.13 reference point.
▪ Preparation is independent of 2.0. Land near the best substations, the EPC partnership, the SPVs and bank lines are all built without 2.0's numbers.
▪ Cost curves are still falling. A 25-year asset started on today's cost curve competes for 25 years with cheaper plants built after it. A later start on a better curve carries less of that exposure.
Sources: Down To Earth – 'Solarising farms, stressing grids: challenges for PM-KUSUM 2.0'; CSE – implementation challenges; Heaven Green Energy – tenant-farmer rules; SME O&M inputs
GreenWealth · PM-KUSUM Component C · 8/15
Notes: https://www.downtoearth.org.in/energy/solarising-farms-stressing-grids-what-are-the-challenges-for-pm-kusum-20
https://www.cseindia.org/implementation-challenges-of-the-pm-kusum-scheme-12284
https://www.heavengreenenergy.com/blog/kusum-tenant-farmer-rules

## Slide 9
Practical challenges on the ground
What operators told us actually goes wrong – beyond the spreadsheet
DISCOM payments run late
Receivables of 60–180 days are normal; the state utility is our only customer for 25 years. The CFA itself only arrives after COD. Model a working-capital line from day one.
We are not an EPC player
The ~Rs 42 L/MW build margin goes to whoever builds. Tender eligibility needs a track record we don't have, so a JV or long-run partnership is unavoidable – and the partner also becomes our 25-year O&M dependency.
Land we lease today may be more than we need
Higher-efficiency modules and trackers keep cutting acres per MW (≈5 today, trending to 3.5–4). A 25-year lease on 5 acres/MW risks paying rent on land a repowered plant will not use.
Existing kit may have to be discarded
Repowering with better modules 8–12 years in can beat nursing an old array. Solar PV modules sit under India's E-Waste (Management) Rules 2022 – end-of-life disposal is our cost and liability.
Feeder separation is a prerequisite
Many 11 kV lines still mix farm and domestic load. Until the DISCOM physically separates the agricultural feeder, FLS cannot start – and that timeline is theirs, not ours.
Rural site realities
Dust and monsoon dips cut yield; cleaning water is scarce in N. Karnataka; module theft and cable vandalism happen; skilled O&M staff must be brought in and retained.
Policy and supply-chain churn
ALMM restricts module sourcing and raises price; duty and GST changes move capex mid-project; tender ceilings keep falling (Rs 3.07 → Rs 2.13).
Capital locked in guarantees
Bid security and performance security (≈ Rs 1 L/MW each) plus the CFA bank guarantee tie up cash for years and shrink the leverage we can raise.
Mitigations, slides 12–15: an early EPC partnership, leases with step-down and repowering clauses, a capex ceiling of Rs 4.5 cr/MW, and written CFA / feeder-separation positions ahead of bidding.
Sources: Down To Earth (DISCOM delays, feeder separation); CSE – implementation challenges; MNRE ALMM orders; E-Waste (Management) Rules 2022; HESCOM RfS (securities); SME inputs
GreenWealth · PM-KUSUM Component C · 9/15
Notes: https://www.downtoearth.org.in/energy/solarising-farms-stressing-grids-what-are-the-challenges-for-pm-kusum-20
https://www.cseindia.org/implementation-challenges-of-the-pm-kusum-scheme-12284
https://solarquarter.com/2025/12/11/hescom-invites-bids-for-108-mw-solar-projects-under-pm-kusum-in-karnataka/

## Slide 10
The alternative offtaker: EIA Labs
The same daytime units, sold to a sister-concern AI lab alongside the DISCOM instead of only to the DISCOM
Rs 6.60
per kWh – KERC HT-2 energy charge for data centres, 2025-26 (+ Rs 345/kVA demand charge, + 36 p surcharge)
70–75%
of a compute facility's operating cost is electricity
1.57 GW
India's installed DC power capacity (Aug 2026), up from 375 MW in 2020
7–12 GW
projected by 2030 (CAGR ~40%); CEA sees 17 GW demand by 2031-32
THE ARBITRAGE
▪ The DISCOM pays the plant Rs 2.13–3.07 per unit
▪ EIA Labs pays the grid ≈ Rs 7 per unit all-in for the same electron
▪ At Rs 6.00 from the plant: EIA Labs saves ~15% on its largest cost line; the plant earns 2× the DISCOM rate
▪ Edge / small facilities are 1% of Indian DC capacity today – the segment a 1–5 MW solar site can serve
WHY IT FITS THESE SITES
▪ Rural substations with spare evacuation, low-cost land, and 300+ sunny days
▪ Daytime AI training / batch inference loads are flexible – they follow the sun
▪ Karnataka already prices DC power in its tariff order (HT-2 category) – the offtaker class exists
▪ Grid supply remains the night-time source; storage is not required on day one
CAVEAT – STATED UP FRONT
EIA Labs' own facility (IT load, cooling, connectivity, 24×7 power conditioning) is a separate and significant build, carried by EIA Labs. That assessment is under way with subject-matter experts; nothing on the next slide assumes GreenWealth funds it. The facility is described throughout as an AI lab.
Sources: KERC Combined Tariff Order 2025 (HT-2); JLL India data-centre mid-year report 2026; IANS / Hans India (8 GW by 2030); Indian Infrastructure (12 GW); IEEFA; tice.news; CEA
GreenWealth · PM-KUSUM Component C · 10/15
Notes: https://data.opencity.in/dataset/kerc-combined-tariff-order-2025
https://www.jll.com/en-in/insights/market-dynamics/india-data-centers
https://ianslive.in/indias-datacentre-capacity-likely-to-touch-8-gw-by-2030--20260914133906
https://indianinfrastructure.com/2026/07/28/indias-data-centre-capacity-to-reach-12-gw-by-2030-says-industry-report/
https://ieefa.org/resources/indias-power-hungry-data-centre-sector-crossroads

## Slide 11
1 MW: DISCOM-only vs GreenWealth + EIA Labs
Same sun, same land bank – a different buyer for most of the units. Cumulative net cash, Rs crore
Chart: Cumulative net cash (Rs crore)
| Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7 | Y8 | Y9 | Y10 | Y11 | Y12 | Y13 | Y14 | Y15
DISCOM only, Rs 3/unit → ≈ year 11.8 | -4.5 | -3.085 | -2.725 | -2.369 | -2.019 | -1.674 | -1.373 | -1.078 | -0.79 | -0.508 | -0.484 | -0.216 | 0.046 | 0.3 | 0.547 | 0.786
70% to EIA Labs @ Rs 6 + 30% FLS @ Rs 3 → ≈ year 7.4 | -5 | -4.015 | -3.352 | -2.695 | -2.045 | -1.402 | -0.811 | -0.227 | 0.348 | 0.914 | 1.222 | 1.771 | 2.311 | 2.842 | 3.363 | 3.875
80% to EIA Labs @ Rs 6.6 + 20% FLS → ≈ year 6.3 | -5 | -4.003 | -3.223 | -2.451 | -1.686 | -0.928 | -0.222 | 0.475 | 1.163 | 1.842 | 2.261 | 2.921 | 3.572 | 4.213 | 4.844 | 5.465
WHAT CHANGES
▪ Annual net cash: Rs 36.5 L → ~Rs 67 L (70/30) / ~Rs 79 L (80/20)
▪ Break-even: ~12 yrs → ~7 / ~6 yrs
▪ Year-15 cumulative: Rs 0.8 cr → Rs 3.9 / Rs 5.5 cr
▪ Solar-side add-on only: dedicated feeder, metering, power conditioning ≈ Rs 0.5 cr
HOW THIS IS STRUCTURED
▪ Two plants on one land bank: 0.3 MW FLS (Plant A – CFA, DISCOM PPA) + 0.7 MW captive (Plant B – supplies EIA Labs)
▪ FLS output cannot be sold to a third party (MNRE FLS guidelines) – hence two plants, not one split plant
▪ Plant B is co-located with EIA Labs, behind the meter – no wheeling charges
▪ EIA Labs PPA at Rs 6.0–6.6; EIA Labs' facility capex sits in EIA Labs, outside this model
Model as slide 6 plus: total capex Rs 5.0 cr across both plants, opex Rs 9.5 L, CFA on Plant A only. EIA Labs price anchored to KERC HT-2 data-centre energy charge (Rs 6.60/kWh). Illustrative.
GreenWealth · PM-KUSUM Component C · 11/15
Notes: Series: DISCOM [-4.5, -3.085, -2.725, -2.369, -2.019, -1.674, -1.373, -1.078, -0.79, -0.508, -0.484, -0.216, 0.046, 0.3, 0.547, 0.786]
Hybrid 70/30 [-5.0, -4.015, -3.352, -2.695, -2.045, -1.402, -0.811, -0.227, 0.348, 0.914, 1.222, 1.771, 2.311, 2.842, 3.363, 3.875]
Hybrid 80/20 [-5.0, -4.003, -3.223, -2.451, -1.686, -0.928, -0.222, 0.475, 1.163, 1.842, 2.261, 2.921, 3.572, 4.213, 4.844, 5.465]
Break-evens {'A_allin': 11.8, 'A_bench': 7.3, 'H_7030': 7.4, 'H_8020': 6.3}

## Slide 12
GreenWealth + EIA Labs: the structure
PM-KUSUM money cannot follow FLS power to a third party – so the investment is split across two plants and two entities on one land bank
GREENWEALTH – developer & land bank
▪ Leases the land from farmers; holds Plant A SPV 100% and Plant B SPV up to 74%
▪ Carries EPC, O&M and the DISCOM relationship for both plants
PLANT A SPV – FLS
▪ Bids the feeder tender
▪ 30% CFA – Rs 1.05 cr/MW on COD
▪ 25-yr DISCOM PPA, ~Rs 2.1–3.0/unit
▪ Output dedicated to the feeder – no third-party sale (MNRE)
PLANT B SPV – CAPTIVE
▪ No CFA
▪ EIA Labs holds ≥ 26% equity and takes ≥ 51% of output → captive status (Electricity Rules 2005)
▪ Private PPA with EIA Labs at ~Rs 6/unit
▪ Co-located, behind the meter
EIA LABS – sister concern, separate entity
▪ Owns and funds the AI-lab facility; buys daytime solar from Plant B at ~Rs 6 vs ~Rs 7 from the grid; grid supplies the night
▪ Carries its own incentive stack (right) and its own business case
Site (tentative)*: Grade-A substation in the Mudhol / Raibag cluster* – open-source shortlist. 1 MW pilot, expandable to 5 MW.
ENTITY
PROVISION
WHAT IT GIVES
PLANT A SPV
PM-KUSUM Component C
30% CFA (Rs 1.05 cr/MW) on COD; 25-yr fixed-tariff PPA
PLANT B SPV
Electricity Rules 2005 – captive
With EIA Labs at ≥ 26% equity / ≥ 51% offtake: exempt from cross-subsidy and additional surcharge
PLANT B SPV
Karnataka RE Policy 2022-27
Captive / group-captive via open access; 100% electricity-duty exemption 8 yrs; stamp-duty exemption; investment promotion subsidy
EIA LABS
Karnataka Data Centre Policy 2022-27
7% capital subsidy on fixed assets outside Bengaluru; 100% stamp-duty exemption; concessional industrial tariff; electricity-duty exemption; green-energy charge reimbursement
EIA LABS
IndiaAI Mission (MeitY)
40% compute subsidy on GPU access (100% for foundational-model training); subsidised GPU-hour rates
BOTH SPVs
Income-tax Act
40% accelerated depreciation in year 1, absorbed against group taxable profits
PM-KUSUM money sits on Plant A only. Every other line is a current, notified state or central policy – none of it depends on PM-KUSUM 2.0.
* Tentative area – open-source desk research only. Sources: MNRE FLS guidelines (PIB); Electricity Rules 2005 r.3; Karnataka RE Policy 2022-27 (KREDL); Karnataka DC Policy 2022-27; IndiaAI Mission (PIB)
GreenWealth · PM-KUSUM Component C · 12/15
Notes: Captive definition: Electricity Rules 2005, Rule 3 – consuming entity holds not less than 26% of ownership and consumes not less than 51% of generation.

## Slide 13
How the power and the load are distributed
1 MW block: 0.3 MW to the feeder, 0.7 MW to EIA Labs by day, grid at night
HOURS
SUN
FARM PUMPS GET
EIA LABS GETS
BALANCE
06:00 – 09:00
Ramp-up
Feeder
Grid + partial solar
Grid
09:00 – 16:00
Peak sun
Feeder (Plant A)
Plant B, up to 0.7 MW
Surplus, if any, banked / exported
16:00 – 18:00
Ramp-down
Feeder
Grid + partial solar
Grid
18:00 – 06:00
Night
Grid (DISCOM)
Grid at HT-2 tariff
–
0.45 M
units / yr → farm feeder (Plant A, 0.3 MW)
1.05 M
units / yr → EIA Labs (Plant B, 0.7 MW)
~30%
of a 0.4 MW 24×7 lab load met by solar; rest from grid
SCALING
The same land bank supports up to 5 MW: 1.5 MW of FLS across the feeder tender and 3.5 MW captive, lifting solar's share of a 24×7 lab load toward 50%. Battery storage, when it earns a premium under PM-KUSUM 2.0, extends Plant B supply into the evening.
WHAT GREENWEALTH GETS
▪ CFA of Rs 1.05 cr/MW on Plant A; 25-yr DISCOM cash flow
▪ Rs 6/unit on Plant B – 2× the DISCOM rate – from a related, creditworthy offtaker
▪ Accelerated depreciation on both SPVs; a saleable operating asset
▪ Annual net cash ~Rs 67 L per MW vs ~Rs 36.5 L DISCOM-only (slide 11)
WHAT EIA LABS GETS
▪ Daytime power at ~Rs 6 vs ~Rs 7 grid – ~15% off the line that is 70–75% of its opex
▪ Captive status: no cross-subsidy or additional surcharge; electricity-duty exemption
▪ 7% capital subsidy, stamp-duty exemption, concessional tariff under the Karnataka DC Policy (outside Bengaluru)
▪ 40% IndiaAI compute subsidy; green-power credentials for clients
Energy split at 1.5 M units/MW/yr. Lab load of 0.4 MW continuous ≈ 3.5 M units/yr; Plant B supplies ≈ 1.05 M. Sources: KERC HT-2 tariff 2025-26; Electricity Rules 2005; Karnataka DC Policy 2022-27; IndiaAI Mission
GreenWealth · PM-KUSUM Component C · 13/15
Notes: MNRE FLS guidelines: feeder-level plants have no provision for selling surplus power; output is dedicated to the feeder under the DISCOM PPA – hence two separate plants.
https://www.pib.gov.in/Pressreleaseshare.aspx?PRID=1678286
https://kredl.karnataka.gov.in/storage/pdf-files/Policy/Karnataka%20Renewable%20Energy%20Policy%202022-27%20Notification%20Copy.pdf
https://www.ahlawatassociates.com/blog/india-data-centre-policy-by-state
https://www.snrlaw.in/data-centres-in-india-opportunity-and-incentives/
https://www.pib.gov.in/PressReleasePage.aspx?PRID=2097709
https://www.outlookbusiness.com/deeptech/artificial-intelligence/govt-offers-100-compute-subsidy-for-foundational-ai-model-development
Mudhol cluster (tentative): Shirol (A, 18 feeders), Uttur, Mantur, Vajramatti, Rannabelagali within ~9–14 km. Raibag has the highest feeders per station (12.7).

## Slide 14
Risks and open questions
What we know we do not yet know
EIA Labs facility economics
Facility capex, cooling and connectivity are a separate build carried by EIA Labs; scoping is under way with SMEs. The upside on slide 11 is conditional on that case closing.
Two-plant structure
FLS output cannot go to a third party (MNRE), so CFA sits on Plant A only. Residual exposure: DISCOM consent, open-access charges and metering for the captive Plant B.
Captive & open access
Wheeling and cross-subsidy surcharges apply if Plant B and EIA Labs are not co-located; the ≥ 26% / ≥ 51% captive test must hold every year.
Tariff ceiling drift
Rs 2.13 (HESCOM C) vs Rs 3.07 (KERC generic): the component bid decides both income and exit value.
DISCOM counterparty
Late payment is the norm; 90–120 day receivables and a working-capital line are part of the base structure.
Land & title
Tenant cultivators, joint pattas, unregistered leases – the failure that surfaces after money is spent.
Coordinates are Google-derived
Suitable for shortlisting; the KPTCL / KREDL GIS layer is the authoritative source for siting.
Terminology & optics
The facility is an AI lab. A 'data centre' beside farmland invites objections the project does not need.
Colour = severity for the decision: red blocks a go-decision until answered; amber shapes the economics; green is execution hygiene
GreenWealth · PM-KUSUM Component C · 14/15
Notes: Open items ahead of capital commitment: EIA Labs facility case; Plant B captive approvals; 2.0 notification terms.

## Slide 15
The message, in one line
Solar is a good sector – but it is heavy capital, and on Component C alone we must be willing to wait 7 years at best (realistically 10–12) to break even, and only then earn.
IF WE WANT THE ANNUITY
Enter Component C as designed. Accept ~7–10 yr break-even. Suits patient capital at ≤ 9% cost of funds.
IF WE WANT VELOCITY
Develop, commission, sell to an InvIT in ~3 yrs. Needs EPC margin in-house and a ≥ Rs 3 tariff for exit value.
IF WE WANT BOTH
GreenWealth + EIA Labs: two plants on one land bank – FLS for CFA, captive solar to EIA Labs at ~Rs 6, DC-policy and IndiaAI incentives on the lab. Break-even ~6–7 yrs, double the annual cash, conditional on the facility case.
Position: capital is committed only after PM-KUSUM 2.0 is notified. The intervening two quarters go to land, the EPC partnership, the EIA Labs offtake agreement and the captive approvals – so that when the terms land, execution follows in weeks.
GreenWealth · PM-KUSUM Component C decision brief · 15/15
Notes: Close: annuity, velocity, or GreenWealth + EIA Labs – and the two-quarter preparation that does not depend on 2.0's numbers.